## Slide 1
Instrumentation EZ
Automated Engineering Document Generation & IODB Validation Platform
Presented to: Management & Executive Leadership
April 2026 | Instrumentation Engineering Team
Instrument List
I/O List
Data Sheet
Cable Schedule
Loop Wiring
IODB Validation
CONFIDENTIAL

## Slide 2
Agenda
What we will cover today
01
Executive Summary
Business case and purpose of the platform
02
Problem Statement
Current challenges in instrumentation engineering
03
Solution Overview
Introduction to Instrumentation EZ
04
System Architecture
How the platform is structured and works
05
Module Deep-Dives
Instrument List · I/O List · Data Sheet · Cable Schedule · Loop Wiring
06
IODB Validation Engine
How validation works, error detection, Excel report
07
Key Benefits & ROI
Quantified time savings and quality gains
08
Demo Walkthrough
Live demonstration flow
09
Future Roadmap
Planned enhancements and scalability
10
Conclusion
Business impact and next steps
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 3
Executive Summary
Instrumentation EZ — purpose, scope, and business value at a glance
What is it? Instrumentation EZ is an internal web-based platform that automates the generation and validation of engineering documents directly from the Instrument & Operations Database (IODB).
Why does it exist? Engineering teams spend 60-70% of document-preparation time on manual data extraction, formatting, and cross-checking — work that is error-prone and non-value-adding. This platform eliminates that burden.
What does it do? It provides 6 integrated modules: Instrument List, I/O List, Data Sheet, Cable Schedule, Loop Wiring — and an IODB Validation Engine that automatically detects data quality issues and logs them in a structured Excel report.
Who benefits? Instrumentation engineers, project leads, DCS/PLC engineers, procurement, and QA teams — anyone who consumes or reviews these deliverables.
Core value: One upload — five documents generated — zero transcription errors — full audit trail of IODB data quality.
>95%
Time Saved
vs. manual process
6
Modules
in one platform
~0
Manual Errors
with automation
100%
Template Safe
formats preserved
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 4
Problem Statement
The hidden cost of manual instrumentation document preparation
Time-Intensive Manual Work
- Copy-pasting data from IODB into every document type
- A single Datasheet takes 15-30 minutes to prepare manually
- 100 instruments = 3-4 weeks of engineering time
- Every IODB revision requires full rework of all documents
High Error Risk
- Transcription errors undetected until client review
- Inconsistencies between Instrument List and Cable Schedule
- Missing values left blank instead of flagged
- No systematic data quality check across the IODB
No Standardisation
- Different engineers produce differently formatted documents
- Template versions mismatched across project phases
- No traceability between IODB version and output document
- Rework caused by late detection of upstream data errors
Industry data: Manual document preparation accounts for up to 40% of engineering labour on mid-size projects — the highest non-value-adding activity on site.
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 5
Solution Overview — Instrumentation EZ
A single platform that turns raw IODB data into finished, formatted engineering documents
Upload once. Generate everything. Validate instantly.
Upload IODB
->
Select Module
->
Configure Options
->
Generate
->
Download Output
Instrument List
I/O List
Data Sheet
Cable Schedule
Loop Wiring
IODB Validation
Built with Python 3.14 · Streamlit · openpyxl · pandas | Runs in any browser — no installation required for end users
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 6
System Architecture
Clean four-layer design — easy to extend, maintain, and deploy
PRESENTATION LAYER
main.py — Streamlit Web Application
Module selector · File upload widgets · Progress indicators · Preview tables · Download buttons · Session-state file caching
v
ORCHESTRATION LAYER
utils/template_processor.py — Pipeline Coordinator
Reads and parses uploaded files · Invokes the correct generator · Validates data shapes · Bundles multi-file ZIP outputs
v
DATA LAYER
utils/file_handler.py — Robust File Ingestion
Auto-detects sheet name & header row · Fuzzy column matching · Content_Types.xml auto-repair · .xls format detection & rejection
v
GENERATION LAYER
utils/generators.py — Document & Validation Engines
5 document generators + 1 IODB Validation engine · Formula preservation · Drawing/shape injection · TBA safety net
INPUT -> IODB.xlsx + Template.xlsx
OUTPUT -> .xlsx / .zip — Ready for issue
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 7
Platform Modules — At a Glance
Five automated document generators + one validation engine
01 Instrument List
Exports any selected IODB columns as a clean, formatted Excel register.
Before: 3-4 hrs
After: < 5 sec
02 I/O List
Auto-suggests I/O columns; produces a DCS/PLC-ready signal register.
Before: 4-6 hrs
After: < 5 sec
03 Data Sheet
Per-tag datasheets from template; batch ZIP export for all tags.
Before: 15-30 min/tag
After: ~2 sec/tag
04 Cable Schedule
JB-grouped, naturally sorted, SPARE-padded cable schedule.
Before: 1-2 days
After: < 30 sec
05 Loop Wiring
Per-tag loop sheets; shapes, lines and formulas fully preserved.
Before: 30-60 min/tag
After: ~3 sec/tag
06 IODB Validation
Scans entire IODB; logs every error with location + type + description.
Before: Manual audit
After: < 10 sec
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 8
Module Deep-Dive: Data Sheet Generator
Batch-generate fully formatted instrument datasheets — one per tag — from IODB + template
How It Works
- Upload IODB source + Datasheet template
- Engine maps template labels to IODB columns using fuzzy matching
- For each selected tag: copy template, fill matched cells
- Formula cells are never overwritten — calculated fields stay live
- Empty IODB values written as 'TBA' (never left blank)
- All datasheets packaged into Datasheets.zip for one-click download
Smart Matching Engine
- 'Line Size (NB)' in template auto-maps to 'line size' in IODB
- Works across any template format — no manual column mapping
- Header row auto-detected even if data starts at row 3-6
- Partial / substring match as fallback for non-standard names
- Case-insensitive across all comparisons
Business Impact
- 100 datasheets in < 4 minutes vs. ~50 hours manually
- Zero transcription errors — IODB is the single source of truth
- Engineers focus on engineering, not copy-paste
- Re-run instantly on any IODB revision
- Consistent formatting across every tag and every project
Supported Use Cases
- IFC (Issued for Construction) datasheet packages
- As-built datasheet generation post-commissioning
- Bid / tender datasheet packages for vendor inquiry
- Internal review packs for engineering sign-off
- Client deliverable compilation for project handover
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 9
Module Deep-Dive: Cable Schedule Generator
Junction-box-grouped, naturally sorted, SPARE-padded cable schedule — in under 30 seconds
Processing Pipeline
- STEP 1 — Load IODB, auto-detect 'Junction Box' and 'Tag No' columns
- STEP 2 — Filter out tags with JB = '-' (unassigned / field instruments)
- STEP 3 — Group all tags by Junction Box reference number
- STEP 4 — Natural-sort each JB group (1, 2, 3 ... 10, not 1, 10, 2)
- STEP 5 — Pad each group to 12 rows with SPARE entries (field-change buffer)
- STEP 6 — Match IODB column names to template headers dynamically
- STEP 7 — Fill template rows; preserve all borders, merged cells, row heights
- STEP 8 — Adjust formula row references when rows are inserted
- STEP 9 — Compact output by removing blank spacer rows
- STEP 10 — Apply Arial 12 centre-wrap formatting to all data cells
Engineering Value
- Mirrors physical wiring layout in the field
- SPARE rows allow field changes without rework
- Formula breakage on row insert — solved
- Multi-JB project: all scheduled in one run
- Output: IFC-ready Cable_Schedule.xlsx
Time Comparison
- Manual: 1-2 days per revision
- With tool: < 30 seconds
- Re-run cost after IODB change:
- Manual: Full rework (hours)
- With tool: Re-click (seconds)
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 10
Module Deep-Dive: Loop Wiring Generator
Per-tag loop sheets with shapes, connectors, and formulas fully preserved
How It Works
- Upload Loop Wiring Input file (tag list + instrument data)
- Locate 'AI Instr' sheet in template (tolerant name matching)
- Read column headers from Row 18, columns W to AR (22 fields)
- For each tag: copy_worksheet() — full template duplication
- Fill Row 19 (W to AR) with matched values from input file
- Formula cells never overwritten — all live calculations preserved
- Empty values written as 'TBA' — no blank cells in output
- Sheet named 'Loop_<TagNumber>' for clear navigation
- Tolerant matching: 'AI-INST ', 'ai instr', 'AI Instr' all work
- Output: Loop_Wiring.xlsx with one tab per instrument
Drawing & Shape Preservation
- openpyxl copy_worksheet() preserves native shapes & styles
- For complex drawings (connectors, P&ID symbols, text boxes)
- that openpyxl cannot round-trip: ZIP-level XML injection
- Drawing XML copied directly into output ZIP after save
- Every generated sheet retains the original template drawings
Business Impact
- 100-tag loop wiring set: ~5 mins vs. ~80 hrs manually
- No risk of missing fields — TBA ensures full coverage
- Template revision: re-run with new template — done
- Consistent sheet naming aids document control
- Directly usable as field loop folder / commissioning pack
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 11
IODB Validation Engine
Automated data quality analysis — catch every error before it reaches a drawing or document
The IODB is the single source of truth for all engineering documents. A single error propagates into every output — Validation stops that.
Analyse
Reads the entire IODB and inspects every row and column for completeness, format compliance, and cross-field consistency.
Detect
Applies a rule library to identify: missing mandatory fields, duplicate tag numbers, invalid signal types, format violations, and cross-reference mismatches.
Report
Generates a structured Excel log with exact cell location (sheet, row, column), error type, severity level, and a plain-English description of what is wrong and why.
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 12
IODB Validation — How It Works
Step-by-step validation logic from raw IODB to error report
1
STEP 1: Load & Parse
IODB uploaded — auto-detect sheet name, header row, and column structure — DataFrame built in memory with all rows and columns preserved
v
2
STEP 2: Schema Check
Verify mandatory columns are present (TAG NO, SERVICE, SIGNAL TYPE, JB, P&ID) — Flag any missing or misnamed columns as schema-level errors
v
3
STEP 3: Row-Level Rules
For every data row: check for empty mandatory fields, duplicate tag numbers, invalid IO types, out-of-range values, and format violations
v
4
STEP 4: Cross-Reference Checks
Cross-validate field relationships: tag appears in loop but not cable schedule, JB assigned but no cable number, signal type conflicts with IO type
v
5
STEP 5: Report Generation
Compile all findings — write structured Excel report with: Sheet, Row, Column, Error Type, Severity (Critical / Warning / Info), Description
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 13
IODB Validation — Error Types & Report Format
Every issue captured with location, type, severity, and plain-English description
Error Category
Severity
Examples
Business Risk
Missing Mandatory Fields
Critical
TAG NO empty, SERVICE blank, SIGNAL TYPE not filled
Document generation produces TBA everywhere; unacceptable for IFC
Duplicate Tag Numbers
Critical
Same TAG NO appears on two rows in the IODB
Two instruments with same tag — wiring conflict, commissioning error
Invalid Signal/IO Type
Warning
Signal type not in approved list (e.g. 'ANALOG OUT' spelled wrong)
DCS I/O assignment fails; loop wiring sheet mismatch
Cross-Reference Mismatch
Warning
Tag in Loop Input not found in Cable Schedule section of IODB
Missing cable entries discovered late — delays field work
Format Violations
Info
JB number format incorrect, P&ID reference format wrong
Document control rejections; non-conformance at client review
Orphaned JB References
Info
JB assigned to tag but JB has no corresponding schedule entry
Field installation cannot proceed without correct JB schedule
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 14
IODB Validation — Sample Report Output
Structured Excel log — exact location, clear description, actionable guidance
Row #
Sheet
Column
Error Type
Severity
Description
14
IODB
SERVICE
Missing Mandatory Field
Critical
Cell is blank. SERVICE is required for datasheet generation.
27
IODB
TAG NO
Duplicate Tag Number
Critical
200-PT-20102 appears on rows 27 and 43. Tag numbers must be unique.
35
IODB
SIGNAL TYPE
Invalid Enumeration
Warning
'ANLAOG IN' is not a recognised signal type. Did you mean 'ANALOG IN'?
52
IODB
JUNCTION BOX
Cross-Ref Mismatch
Warning
Tag 200-FIT-20105 references JB-03 but no cable entry found for JB-03.
61
IODB
P&ID NO
Format Violation
Info
P&ID reference '1234-E-5678-001' does not match expected format.
78
IODB
LOOP NO
Empty Recommended Field
Info
LOOP NO is blank. Loop wiring sheet will be generated without loop reference.
91
IODB
IO TYPE
Inconsistency
Warning
IO TYPE = 'DO' but SIGNAL TYPE = 'ANALOG IN'. These are contradictory.
Report saved as IODB_Validation_Report.xlsx — shareable with project team and QA lead for resolution
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 15
Key Benefits & Return on Investment
Quantified impact across a typical 200-instrument project
>95%
Time Saved
Document prep from weeks to minutes
~170
Hrs / Project
Saved per 100-instrument project
~0%
Error Rate
Transcription errors eliminated
100%
Template Fidelity
All formats, formulas & shapes preserved
Free
Re-Runs
Re-generate any time the IODB changes
Deliverable
Manual Effort (100 instr)
With This Tool
Saving per Project
Instrument List
3-4 hours
< 5 seconds
~3.5 hours
I/O List
4-6 hours
< 5 seconds
~5 hours
Data Sheets
50-80 hours
< 1 hour
~65 hours
Cable Schedule
16-24 hours
< 0.5 hours
~20 hours
Loop Wiring
50-100 hours
< 1 hour
~75 hours
IODB Validation
Manual audit (if done at all)
< 10 sec
Defect prevention
TOTAL
~120-200 hours
~3 hours
~170 hours saved
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 16
Live Demo — Walkthrough Steps
How to demonstrate the tool in 8 minutes for a management audience
1. Open the App
Navigate to the Streamlit URL in any browser — no login, no install. Show the clean header, sidebar navigation, and module list.
2. Upload IODB
Upload IODB.xlsx once. Show the green 'Loaded Files' indicator — file persists across all modules.
3. Instrument List
Select 5-6 key columns, click Generate, download instantly. Open the file to show correct data and formatting.
4. Data Sheets
Upload Datasheet template, select 3 tags, Generate, download ZIP. Open one .xlsx — show all fields filled, formulas intact.
5. Cable Schedule
Upload CS template, click Generate, open output. Show natural-sorted JBs, SPARE rows, and preserved formatting.
6. IODB Validation
Click Validate — completes in < 10 seconds. Open IODB_Validation_Report.xlsx — walk through a Critical error row.
7. Highlight a Fix
Fix the flagged error in the IODB, re-upload, re-validate. Show the error disappears — close the feedback loop live.
8. Summary
Recap: same IODB, 5 documents + validation report — all in under 5 minutes. Ask: 'How long would this take manually?'
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 17
Future Roadmap & Scalability
The platform is designed to grow — new modules, cloud deployment, and AI integration
Phase 1 — Complete
Instrument List Generator
I/O List Generator
Data Sheet Generator (batch ZIP)
Cable Schedule Generator
Loop Wiring Generator
IODB Validation Engine
Session-state file caching
Robust edge-case handling
Phase 2 — Next Quarter
Enhanced validation rule library
PDF export option for datasheets
Multi-template support per module
Automatic revision tracking
Inline IODB edit and re-validate
Email / MS Teams delivery
User activity log for audit trail
Phase 3 — Strategic Vision
Cloud deployment (Streamlit Cloud / Azure)
Role-based access control (RBAC)
Integration with project database (SQL)
IODB change-diff between revisions
AI-assisted column mapping & suggestions
Approval workflow with digital stamp
Multi-project / multi-discipline support
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 18
Built for the Real World — Technical Robustness
Designed to handle inconsistent files, naming variations, and edge cases gracefully
Auto Sheet Detection
Tries exact, case-insensitive, then substring match. 'AI-INST ', 'AI Instr', 'ai instr' all resolve correctly.
Header Row Auto-Detection
Probes rows 0-10 per sheet; scored by tag-column presence and non-empty column count. Works with metadata-heavy files.
Fuzzy Column Matching
Template labels matched to IODB headers via normalised substring comparison — no manual mapping ever required.
Content_Types.xml Repair
Synthesises a valid [Content_Types].xml from the ZIP manifest when a template was repaired by Excel and is corrupt.
Formula Preservation
Every generator checks for '=' prefix before writing. Calculated fields remain live and correct in every output.
Drawing / Shape Injection
ZIP-level XML copy injects complex drawings (connectors, P&ID symbols) that openpyxl cannot round-trip natively.
Column Name Tolerance
'Tag_nummber', 'Tag No.', 'TAG NUMBER' — all auto-resolve to the same tag column. No user action needed.
File Format Guard
Old .xls (OLE2) files detected by magic bytes and rejected with a clear 'Please save as .xlsx' message — not a crash.
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 19
Conclusion — Business Impact Statement
Instrumentation EZ delivers measurable, lasting value across every project phase
This platform fundamentally changes how instrumentation engineering documents are produced — faster, error-free, and production-ready from day one.
Operational Impact
- Document turnaround from days to minutes
- ~170 engineering hours saved per project
- Re-generation on IODB change costs zero extra effort
- All 5 document types from a single data upload
- Zero manual formatting — template fidelity guaranteed
Quality Impact
- Transcription errors eliminated by design
- IODB Validation catches data issues at source
- TBA safety net — no blank cells in any output
- Consistent document style across all engineers
- Audit trail: validation report documents QA evidence
Strategic Impact
- Frees senior engineers for value-added work
- Reduced rework cost at client review stage
- Platform scales to any project size instantly
- Foundation for future AI and cloud integration
- Competitive advantage in tender & execution speed
Recommended Next Step: Approve platform for live project deployment and initiate Phase 2 enhancements
Instrumentation EZ | Internal Presentation | 2026 | Confidential

## Slide 20
Thank You
Instrumentation EZ — Key Takeaways
◆ 6 integrated modules — document generation and data validation in one platform
◆ ~170 engineering hours saved per 100-instrument project
◆ IODB Validation catches data errors before they reach any deliverable
◆ Zero transcription errors — all outputs flow directly from IODB
◆ Built for extensibility — cloud, AI, and workflow integration ready
Built with Python · Streamlit · openpyxl | GitHub: AdithyaChoudhry/IEZ
Questions & Discussion